## Slide 1
Towards Sub-Nyquist Tissue Doppler Imaging
Avinoam Bar Zion, Martino Alessandrini, Jan Dhooge, Dan Adam and Yonina Eldar

## Slide 2
Why ?
Compressed Sensing (CS)
Tissue Doppler
Currently:
  Limited to few measurement points
  Tradeoff between spectral and spatial resolution
  Signals are sampled at frequencies higher than the Nyquist rate
Marwick, et al. ”Myocardial imaging: tissue Doppler and speckle tracking,” 2008.
B-mode
Spectral Doppler
few measurement points
High data volumes

## Slide 3
The system of equations:
KxP
KxK
KxN
NxM
.
.
.
.
.
.
.
.
.
.
.
.
Samples
PSF
Fourier
Representation
(sparse)
fast time
frequencies
pulses
MxP
Fourier
T
Sampling rate reduction via CS
The sparse representation matrix A is estimated from the measurements by solving an l1 minimization problem

## Slide 4
The representation matrices (40% Fast Time):
With 20% of the pulses the map’s correlation coef. R > 0.8
20% Slow Time
50% Slow Time
100% Slow Time
Doppler Frequency
Depth
Doppler Frequency
Doppler Frequency
Results: Depth-Doppler Maps

## Slide 5
Spectral estimations from specific depths concatenated to produce spectral Doppler images
30% Slow Time
50% Slow Time
100% Slow Time
Depth = 6.2 cm; 40% fast time
Septum
Scan
Plane
RESULTS: tdi PLOTS

## Slide 6
RESULTS: CS tdi dEMO
A demo version was implemented on a Verasonics Vantage 256™ system

## Slide 7
TDI signals estimated from sub-Nyquist samples:
  Using a subset of the fast time frequencies
  Non-uniformly space stream of pulses
Facilitating increased imaged sector
Reduced data volumes -> hand-held / wireless systems
Xampling:
Sub Nyquist Sampling
summary

## Slide 8
SAMPL Lab, Technion
Ido Cohen
Shai Yagil
Regev Cohen
Or Dicker
Tanya Chernyakova
Deborah Cohen
Dan Adam’s Lab, Technion
Amit Livneh
Hanan Khamis
Grigoriy Zurakhov
Verasonics
Thank you
This project has received funding from the European Union's Horizon 2020 research and innovation programme under grant agreement No. 646804-ERC-COG-BNYQ0