## Slide 1
Resolution Loss without Optical Blur
Tali Treibitz
Alex Golts
Yoav Y. Schechner
Technion , Israel
1
Notes: Good afternoon. Our work deals with analysis of cross-modal signals. Specifically, with audio-visual signals.

## Slide 2
14
airlight
A
0
1
z
scattering
direct transmission
D
object radiance
L
object
total intensity
I
0
z
Schechner, Narasimhan, Nayar

## Slide 3: Haze
airlight
object
transmittance
Schechner et al., Applied Optics ‘03
15
Notes: haze

## Slide 4: Pointwise Degradations
object
pointwise attenuation:
vignetting
atmosphere attenuation
additive component:
reflection
glare
path radiance
noise
Treibitz & Schechner, Recovery Limits in Pointwise Degradations
17
Notes: What is the relation of all this to computer vision?
There are many works that were done by people in this room where the common property is that there is no blur,
Where the degradation is pointwise.
Major part is: estimate t and A, compensate to get L.
Thus, the limits are effective

## Slide 5: Pointwise Degradations
object
pointwise attenuation
noise
Treibitz & Schechner, Recovery Limits in Pointwise Degradations
reduce SNR even if known
additive (positive) bias
18
Notes: 5
Note that because of signal dependent photon noise the additive component reduces the input SNR So even if your reconstruction method precisely estimates that degradation terms, the reconstruction is still limited.
This analysis is not only theoretical. It has practical implications.
Now, we can tell if any reconstruction method can detect an object in a certain size, with a certain contrast under given noise levels. I am going to demonstrate it in the case of haze.

## Slide 6: Noise: Object size matters?
19
Notes: Let’s see what happens when we add noise.
Small details disappear

## Slide 7: Noise: Object size matters?
20
Notes: As we add noise the smaller objects like this branch start to disappear, while the larger ones stay

## Slide 8: Noise: Object size matters?
21

## Slide 9: Noise: Object size matters?
22
Notes: Branch disappears as noise increases
There is no blur- but details still disappear
How can it be- there is no LPF, and still small details disppear
Noise induces a LPF- this is what the work is about

## Slide 10
depends on:
noise level
object  background intensity difference
object size
quantify this dependency !
Prior art: resolution limits due to optical blur
here: no optical blur
Visibility Under Noise
23
Notes: 10
So, visibility under noise depends of course on the noise level,
Obviously, it also depends on the intensity differences between the signal and the background
(same intensity-can’t see),
And- it also depends on the object size! and in this work we quantify this dependency
I want to emphasize that previous works have analyzed how noise affects resolution under blur, for example, when doing a deconvolution
But- here we assume no blur

## Slide 11: Previous criteria
Is there something there?
Is it a tank?
What type is it?
Johnson charts:
identification | recognition | orientation | detection | 
7 | 3.5 | 1.2 | 0.75 | tank
minimum line pairs for 50% success

## Slide 12: NIIRS- National Image Interpretability Rating Scales
Identify the wing configuration (e.g., straight, swept, delta) of all large aircraft (e.g., 707, CONCORD, BEAR, BLACKJACK). ..
Detect large hangars at airfields. Detect large static radars (e.g., AN/FPS-85, COBRA DANE, PECHORA, HENHOUSE), Detect military training areas...
Detect a medium-sized port facility and/or distinguish between taxi-ways and runways at a large airfield.
Interpretability of the imagery is precluded by obscuration, degradation, or very poor resolution
Identify small light-toned ceramic insulators that connect wires of an antenna.
Identify vehicle registration numbers (VRN) on trucks.
Identify screws and bolts on missile components. ..
0
1
2
3
9

## Slide 13
pattern visible
Treibitz & Schechner, Recovery Limits in Pointwise Degradations
24

## Slide 14: Where is the Cutoff?
pattern visible
pattern invisible
calculated analytically!
Treibitz & Schechner, Recovery Limits in Pointwise Degradations
Input SNR
25
(frequency)
Notes: 14
This is the whole image
We took a signal with increasing frequency and added noise with decreasing variance
Signal to noise ratio (SNR) increases
In high frequencies even relatively low noise hides the pattern
Low frequencies- even under high noise the pattern is visible
In the same SNR- low freqs are visible, high are not
We can draw a line (try to) that separates the areas where the pattern is visible from the areas where it’s not
If I’d draw it manually, this is where I’ll do it
This line was calculated analytically- I’ll explain how

## Slide 15
(frequency)
Treibitz & Schechner, Recovery Limits in Pointwise Degradations
26
Cutoff Per Success Rate
success rate 50%
Input SNR
Notes: 15
This is the whole image
We took a signal with increasing frequency and added noise with decreasing variance
Signal to noise ratio (SNR) increases
In high frequencies even relatively low noise hides the pattern
Low frequencies- even under high noise the pattern is visible
In the same SNR- low freqs are visible, high are not
We can draw a line (try to) that separates the areas where the pattern is visible from the areas where it’s not
If I’d draw it manually, this is where I’ll do it
This line was calculated analytically- I’ll explain how

## Slide 16: Noise Suppression in the HVS
Theoretical Neuroscience, Dayan & Abbott
frequency (cycles/degree)
response of receptive field
low noise
high noise
We derive: fundamental analytical model
Model: simple linear denoising
not a denoising method
28
Notes: The human visual system suppresses noise and demonstrates this behavior
In this curve you can see that under high noise, high frequencies are suppressed more
That’s why you managed to see, the eye is doing an averaging action
We do not analyze the HVS, but we want to know the limits of every system
We use tools of simple linear systems- that allow us to analyze frequency response
We calculate the limits of optimal linear systems- will apply also to suboptimal

## Slide 17: SNR Improvement by Averaging
signal
noise
Treibitz & Schechner, Recovery Limits in Pointwise Degradations
- SNR change after averaging
29
Notes: Linear systems-> fourier decomposition
As we work with linear systems, we can look at each frequency separately.
I want to stress that I don’t suggest here a denoising method, I just want to know the limits of an optimal linear LPF.
Linear operation on a sinus- the frequency does not change, only its amplitude changes, in the factor of the system’s response
On noise- decreases the noise
so there is a change in SNR
So averaging with a window affects both the signal and the noise, therefore we understand there is a change in SNR

## Slide 18: Different Sizes of Windows
too big for signal
too small for noise
Treibitz & Schechner, Recovery Limits in Pointwise Degradations
30
Notes: 18
What size of a window should we take?
If the window is too big for the frequency- it averages it out
If it’s too small- we could average more noise
So we understand the SNR change depends on the frequency and the window size

## Slide 19: Averaging by Optimal Window
Treibitz & Schechner, Recovery Limits in Pointwise Degradations
31
Notes: For each frequency, there is an optimal window size- suppresses as much noise without averaging out the frequency
So the ability to improve the SNR depends on the frequency

## Slide 20: SNR Improvement by Averaging
depends on frequency!
Treibitz & Schechner, Recovery Limits in Pointwise Degradations
same plot for a Gaussian filter
32
Notes: Plugging in the expression for reduction in signal and reduction in noise results in the following function for SNR improvement
In the highest frequency- C equals 1: no change
In low frequencies- big improvement

## Slide 21: Output SNR
Treibitz & Schechner, Recovery Limits in Pointwise Degradations
Input SNR
(frequency)
33
Notes: 21
This is how our pattern looks after optimal averaging- we can see that the averaging made the pattern clearer, but no new details are revealed
This is the row were the input SNR was 1, now after averaging the location where the output SNR is 1 depends on the frequency, as you can see in the plot- and this is how we got the previous cutoff curve.
Now, if we know our vision system requires an SNR of 1- and we know the input SNR, we can determine the cutoff frequency using this plot. If the input SNR is higher- the cutoff is higher, if we require a lower SNR, also the cutoff is higher.
But how can we determine what is the output SNR that we need?

## Slide 22: Cutoff Per Success Rate
success rate 70%
success rate 40%
Treibitz & Schechner, Recovery Limits in Pointwise Degradations
Input SNR
(frequency)
34
Notes: 22
So now we can convert the SNR values in the previous plot to success rate.
So now we established a general framework for relating a desired success rate and input SNR to the cutoff frequency.
This is a general framework that does not depend on the imaging model. The imaging model only determines the input SNR. Our only assumption here was that there is no blur

## Slide 23: Vision Success is Probabilistic
SNR=2/3
SNR determines chances of visibility
visible
invisible
Treibitz & Schechner, Recovery Limits in Pointwise Degradations
35
Notes: For example, here we have an image of a dark square on a bright background
With a lower SNR- we still see the coarse details, but the fine details disappear
one side is visible, and the other is not!
But the same SNR- conclusion: SNR influences chances

## Slide 24: Success within a Confidence Interval
- success rate
SNR
Treibitz & Schechner, Recovery Limits in Pointwise Degradations
Object is visible if
…depends on SNR and..
36
Notes: 24
Say we have a signal in a field of noise.
The signal is visible if the noise field does not overwhelm the signal.
Say we have a signal in a field of noise.
The signal is visible if the noise field does not overwhelm the signal.
But- the noise is a random variable, so under the same distribution, it can sometimes be smaller than the signal and sometimes higher.
What is the probability that the noise is smaller than the signal? Of course it depends on the SNR
And on the distribution.
The probability for a random variable to be lower than a certain threshold is termed the confidence interval.
For a gaussian noise, the probability of the noise to be smaller than it’s STD is 68%.
This leads us to this plot that shows the relation between success rate and SNR. An SNR of 1 gives a 68% success rate in detection, lower SNR gives us higher success rate. We see that we gain a lot by improving low SNR values, and less as the input SNR increases.

## Slide 25: Success within a Confidence Interval
25
- success rate
SNR
Treibitz & Schechner, Recovery Limits in Pointwise Degradations
what is the probability for correct detection?
depends on SNR
object pixel
background pixel
visibility is kept if edge keeps sign
%(sign kept) - %(wrong sign)
noisy
clear
Notes: 25
The signal is visible if the noise field does not overwhelm the signal.
Is the noise greater than the signal? Of course it depends on the SNR
And on the distribution.
N is a random variable, what is the chance that is lower than a certain threshold?
This is expressed as a confidence interval
For example here for a white gaussian noise
Increasing above 1.5 doesn’t give much
More details in the paper

## Slide 26: Determining Resolution Limits
system input SNR
cutoff for ρ=70% success
frequency
Treibitz & Schechner, Recovery Limits in Pointwise Degradations
37
Notes: Now we can use the curve we plotted for 70% success to determine the cutoff frequency
This is a fundamental result- depending on the system input SNR and the desired success rate- we can determine the cutoff frequency
Note that there is a cutoff even if there is no blur! This fundamental result does not depend on the type of degradation

## Slide 27: Pointwise Degradations
pointwise attenuation:
vignetting
atmosphere attenuation
additive component:
reflection
glare
haze
noise
Treibitz & Schechner, Recovery Limits in Pointwise Degradations
38
Notes: What is the relation of all this to computer vision?
There are many works that were done by people in this room where the common property is that there is no blur,
Where the degradation is pointwise.
Major part is: estimate t and A, compensate to get L.
Thus, the limits are effective

## Slide 28: Noise Model
Nikon D100
photon noise dominates
39
Treibitz & Schechner, Recovery Limits in Pointwise Degradations
Notes: what is the noise model?
it has a signal independent component, and photon noise- which is signal dependent
as you can see from the example calibration of our camera- because of photon noise, the noise variance increases with the signal
This can also be seen in this demo.

## Slide 29
Detector (pixel)
50% quantum efficiency
Schechner
Photon (shot) Noise
9
Electrons
Photon
or
e
{
nothing
either

## Slide 30
50% quantum efficiency
Schechner
10
Photons
Electrons
e
{
nothing
e
e
either
Photon (shot) Noise

## Slide 31: SNR per size (frequency)
Treibitz & Schechner, Recovery Limits in Pointwise Degradations
41
Notes: We found a connection between the SNR to detection.
Now, how do we calculate the SNR?
We showed a model for the noise
How do we define the signal?
The signal- depends on the application
We look at the difference between the object and its background
This can vary according to size
And is attenuated

## Slide 32: Resolution Limits in Haze
distance [km]
limit due to pixel size
limit due to atmosphere
Treibitz & Schechner, Recovery Limits in Pointwise Degradations
minimal visible object size[m]
reciprocal to
42
Notes: We’ll calculate the limits of dehazing- does not matter which dehazing method
The red is the geometrical limit, and our analysis yielded the blue limit- details in the paper

## Slide 33
(frequency)
Treibitz & Schechner, Recovery Limits in Pointwise Degradations
43
Cutoff Per Success Rate
success rate 50%
Input SNR
Notes: 33
This is the whole image
We took a signal with increasing frequency and added noise with decreasing variance
Signal to noise ratio (SNR) increases
In high frequencies even relatively low noise hides the pattern
Low frequencies- even under high noise the pattern is visible
In the same SNR- low freqs are visible, high are not
We can draw a line (try to) that separates the areas where the pattern is visible from the areas where it’s not
If I’d draw it manually, this is where I’ll do it
This line was calculated analytically- I’ll explain how

## Slide 34
Haze in the Galilee
Treibitz & Schechner, Recovery Limits in Pointwise Degradations
average of 50 frames
raw frame
limit due to noise and not blur
44
Notes: We demonstrate that in a real life example
Here we see big details but the small ones are lost.
You might argue that this is because of atmospheric blur or blur in the imaging system.
To show you that it’s not due to blur, I averaged 50 images- this only reduced noise, and now the objects are visible
34

## Slide 35
What now?
What are the reconstruction limits?
What is the minimal detectable object size?
What camera noise properties are acceptable for detection?
…
45
Notes: You did works about glare, separation, reconstruction, in this conference there are new works
With this analysis you can calculate which object size you can recover, which camera you need

## Slide 36: Imaging in Haze
Treibitz & Schechner, Polarization- Beneficial for Visibility Enhancement?
46
Notes: Haze deteriorates visibility in images- as you can see in this example.
The haze is partially polarized- this means that is you look at the vector of the electrical field- it has one direction that is more dominant than others.
How can we exploit that?

## Slide 37: Haze Through a Polarizer
Treibitz & Schechner, Polarization- Beneficial for Visibility Enhancement?
best polarized image
47
Notes: We can mount a polarizer such that it’ll block the dominant angle
What happens then?
The polarizer blocks part of the light- so the image darker

## Slide 38: Haze Through a Polarizer
Treibitz & Schechner, Polarization- Beneficial for Visibility Enhancement?
single frame- used by photographers
increased exposure time
best polarized image
48
Notes: But it blocks more airlight than signal
Thus, if the exposure time is increased, the result is an image with a better contrast.

## Slide 39: Dehazing using a Polarizer
Treibitz & Schechner, Polarization- Beneficial for Visibility Enhancement?
two frames- Schechner et al.
post-processing 2 frames
best polarized image
worst polarized image
49
Notes: Another option is to acquire 2 polarized frames and post process them.
This is the result. The visibility seems to be much better and seems that the problem is solved. This method requires extra hardware and effort.
The question is, how much does it help? is it worth it?
This is a general question- each of the results I showed you here might be further post processed- using
I want to emphasize that we ask this question in the context of detection- i.e., where can we detect more objects?

## Slide 40
goal: object detection
local contrast stretch- OK
Treibitz & Schechner, Polarization- Beneficial for Visibility Enhancement?
Is it worth using a polarizer?
unpolarized image
best polarized image
post-processing 2 frames
rarely!
under the constraint of equal acquisition time
50
Notes: 40
To look for the objects we can zoom in and do local contrast stretch in areas with uniform distances
So how can we give an decisive answer for that question?

## Slide 41
degree of polarization
Using a Single Polarized Image
Best polarized image
I
min
51
Treibitz & Schechner, Polarization- Beneficial for Visibility Enhancement?
Notes: Haze in the atmosphere is partially polarized
therefore, mounting a polarizer, reduces the airlight relative to the signal in the image
There is one angle of the polarizer where the airlight is minimal, so this is the best image that can be captured with a single polarizer
Larger p means that the polarizer reduces more airlight

## Slide 42: SNR Comparison

52
Treibitz & Schechner, Polarization- Beneficial for Visibility Enhancement?
Notes: 42
so if we compare SNR in the unpolarized frame and the polarized frame- the SNR is the polarized frame is higher (uniform distances)
but- we pay for that with increased exposure time
so the fair comparison is to compare images taken under the same acquisition time. If we just increase exposure time, the image will be saturated. so we can use the available time to take a few frames and average them. It is easy show that the best strategy is dividing the time equally between the frames- and then the SNR increases by root of the number of frames. Then, the SNR in the unpolarized image is higher

## Slide 43
A Single Saturated Frame
Treibitz & Schechner, Polarization- Beneficial for Visibility Enhancement?
SNRpolarized
SNRunpolarized
maximal value in nature
53
Notes: 43
P is the dop
We see there is an improvement, but this is under the assumption that the whole image has uniform distances
i.e., the exposure time of the polarized image is adjusted according to the area we want to detect

## Slide 44: SNR Comparison

equal acquisition time
technical details in the paper
acquisition time = exposure time X number of frames

54
Notes: 44
so if we compare SNR in the unpolarized frame and the polarized frame- the SNR is the polarized frame is higher (uniform distances)
but- we pay for that with increased exposure time
so the fair comparison is to compare images taken under the same acquisition time. If we just increase exposure time, the image will be saturated. so we can use the available time to take a few frames and average them. It is easy show that the best strategy is dividing the time equally between the frames- and then the SNR increases by root of the number of frames. Then, the SNR in the unpolarized image is higher

## Slide 45
Treibitz & Schechner, Polarization- Beneficial for Visibility Enhancement?
Same Total Acquisition Time
p<0.4
in our experiments
SNRpolarized
SNRunpolarized
maximal value in nature
55
Notes: 45
This is the plot for 2 different optical distances
We see there is an improvement, but this is under the assumption that the whole image has uniform distances
i.e., the exposure time of the polarized image is adjusted according to the area we want to detect

## Slide 46: Experiment
Wide field of view
average of 2 frames
Treibitz & Schechner, Polarization- Beneficial for Visibility Enhancement?
same total acquisition time
56
Notes: 46
Here are some example
Imin is noisier even in the single case as the exposure time is not adjusted

## Slide 47: SNR Comparison
dehazing

technical details in the paper
optimal exposures
equal acquisition time
57
Notes: 47
now we compare the SNR with an unpolarized image taken under the same total acquisition time
The 2 polarized images are linearly combined with weights that depend on the degree of polarization

## Slide 48: Advantages of Polarization
distance map
contrast stretch in non-uniform distances
restoring color
compensating for attenuation
58
Notes: This result seems to contradict previous results- some of them done in our lab about polarization based dehazing
But it doesn’t. No polarization based dehazing method have shown to reveal objects that were otherwise invisible
Our analysis assumed that we do a very local contrast stretch and look for objects. Dehazing performs on the whole image, restores color and compensates for attenuation
It also provides a distance map

## Slide 49
Freq cutoff – due to noise – without imaging blur
Relation between cutoff and success rate
Application: limits in pointwise degradations
Limits in Pointwise Degradations
Case study of performance trade-offs
59
Notes: To conclude- we saw that noise imposes a frequency cutoff even with no blur
We gave the relation between cutoff and success rate
And showed how to apply it for cv applications
Now, that we established the relation between SNR and visibility, we can analyze what is the SNR benefit in a certain reconstruction scheme
Once we have the SNR benefit, we can know what was the visibility improvement due to this reconstruction method

## Slide 50
Cutoff frequency in color imaging
What is the smallest recoverable object size (maximum cutoff frequency) per success rate ρ and a given scenario?
Performance prediction
System design
Understanding the benefit of color
Motivation:

## Slide 51
Linear, space-invariant imaging systems
LSI system
Limiting frequency
(Object size)
Minimum resolvable Contrast / Temperature Difference
Modulation transfer function

## Slide 52
Frequency response and Сutoff
Optical blur
Pointwise effects
Single channel
Color
Full field
3-CCD
Bayer
G | R | G | R
B | G | B | G
G | R | G | R
B | G | B | G
A. Golts and Y. Y. Schechner – “Cutoff due to pointwise degradations in color images” – In review, JOSA A.
A. Golts and Y. Y. Schechner – “Spatial frequency response of Bayer color image formation” – In review, JOSA A.
Wikipedia

## Slide 53
Pointwise degradations
Object
Multiplicative component
Additive component
Random noise
Bayer sampling
Atmosphere attenuation
Vignetting
Bobrov & Schechner
http://www.bokashii.com/vignette/
http://elynxsdk.free.fr/API/html/convert_bayer.html
Reflection
I
I
T
Schechner et al, ICCV 99
Haze
Schechner et al, Applied Optics ‘03

## Slide 54
Bayer color sensors
How to quantify the frequency response due to
Bayer sampling and interpolation?
G | R | G | R
B | G | B | G
G | R | G | R
B | G | B | G
Color
Scene
Interpolation/ Demosaicking
R | R | R
R | R | R
R | R | R
G | G | G
G | G | G
G | G | G
B | B | B
B | B | B
B | B | B
Sampling
(Space-Variant)

## Slide 55
Linear, space-invariant imaging systems
LSI system
Bayer is not LSI
We assume linear interpolation
How to assign MTF for such system?

## Slide 56
Previous work
Y. Elor, E. Pinsky, and A. Yaacobi – “MTF for bayer pattern color detector”.
In Proc. SPIE, volume 6567, 2007
G | R | G | R
B | G | B | G
G | R | G | R
B | G | B | G
B/W
Scene
Interpolation/ Demosaicking
Sampling
(Space-Variant)
White balance
Analysis in 1D, Assumed integration in the vertical direction
We perform a full 2D analysis, and verify by simulation

## Slide 57
Color signal representation
A test on ~1000 natural images shows high correlation
between the RGB Fourier phase components
Input to Bayer system:
L.G. Shapiro
Associated Press

## Slide 58
Bayer simulation
Color signal:
Bi-linear interpolation

## Slide 59
Bayer simulation
DTFT

## Slide 60
Bayer simulation

## Slide 62
Bayer color sensors
For an LSI system, this definition coincides with the MTF
Variant
Extension of MTF to space-variant systems:
Spurious response
Elor et. Al - 2007

## Slide 63
Bayer sampling frequency response
Spurious response

## Slide 64
Total frequency response

## Slide 65
Bayer sampling
Raw Bayer signal
G | R | G | R
B | G | B | G
G | R | G | R
B | G | B | G
Ideal signal

## Slide 66
Bayer sampling
Spurious Response

## Slide 67
Bayer linear interpolation
Raw Bayer signal
Interpolation/ Demosaicking
Interpolated signal

## Slide 68
Bayer linear interpolation
B | G | B
G | R | G
B | G | B
G | R | G
B | G | B
G | R | G
G | B | G
R | G | R
G | B | G
R | G | R
G | B | G
R | G | R
R
G1
G2
B
4 pixel types
Interpolation kernels
Example -
Bi-linear:
…

## Slide 69
Bayer linear interpolation

## Slide 70
Total frequency response

## Slide 71
Bayer simulation
DTFT

## Slide 73
Bayer spatial frequency response
- Summary
Analytical expressions for Bayer SFR – VMTF and parasitic SR
2D analysis
Account for color input
Account for both Bayer sampling and interpolation.
Verified by simulation.

## Slide 74
Full-field color systems
Several full sensors
No spatial resolution compromise
3-CCD / N-CCD
FOVEON technology
Time multiplexing
www.foveon.com
Wikipedia
Optec Inc.

## Slide 75
Previous work
T. Treibitz and Y. Y. Schechner – “Resolution loss without imaging blur”
JOSA A, 2012
Found limits for single-channel signals
(frequency)
Visible pattern

## Slide 76
Previous work
T. Treibitz and Y. Y. Schechner – “Resolution loss without imaging blur”
JOSA A, 2012
Found limits for single-channel signals
Input SNR
(frequency)

## Slide 77
Full field color systems
Background level

## Slide 78
Filtering in the color domain
How can we account for color while using results of previous work (pan-chromatic)?
Spectral filtering (fusion)
T. Wang, C. C. Shaw and C-C. Li– “Pixelwise fusion for optimizing SNR in multiple-plate computed radiography imaging”.
IEEE Trans. on Medical Imaging, 1999
We seek α which maximizes the SNR:
Signal amplitude
Noise
Panchromatic case with enhanced SNR

## Slide 79
Resolution improvement due to color fusion
The optimal SNR (after fusion) satisfies:
We quantify resolution improvement by comparing the following
Detector
1
2
3
4
N
…

## Slide 80
Limitation of the improvement


Low variability SNR
High variability SNR

## Slide 81
Hyperspectral image example
A. Chakrabarti and T. Zickler. Statistics of real-world hyperspectral images.
IEEE CVPR, pages 193–200, 2011
31 spectral channels
We added synthetic noise
Signal estimation:

## Slide 82
Hyperspectral image example
Low variability SNR
Panchromatic
Optimal color fusion
Color
High variability SNR
Color
Optimal color fusion
Panchromatic

## Slide 83
Simulation
Dominant photon noise
,
Color
Panchromatic
Optimal color fusion

## Slide 84
Full-field sensors - Summary
Color fusion for optimal SNR
Analytical expression for the optimal SNR and enhancement factor.
Limiting cutoff frequency in color

## Slide 85
Summary
Modeling of Bayer 2D spatial frequency response accounting for sampling and linear demosaicking.
Spectral filtering for optimal SNR.
Quantify object recovery limits in full-field color systems.

## Slide 86
Further directions
Account for noise and limiting cutoff frequency in Bayer imaging systems .
G | R | G | R
B | G | B | G
G | R | G | R
B | G | B | G

## Slide 87
Further directions
Study resolution limits and possible enhancement in other domains where low SNR and resolution is a common problem:
Medical imaging, thermal, THz, MMW…
Ratheon Company
S. Bobrov and Y. Y. Schechner

## Slide 88
Further directions
Extend our model for non white Gaussian noise.
Dominant fixed-pattern noise in thermal imaging.
A. Averbuch et. al.

## Slide 89
Further directions
New demosaicking algorithms based on our Bayer spatial frequency response model.

## Slide 90
Further directions
Design CFAs other than Bayer based on a desired frequency domain performance.
Consider unified design of CFA + interpolation kernels.
Yasuma et. al.
Fujifilm