## Slide 1: Distributed Adaptive Routing for Big-Data Applications Running on Data Center Networks
* Mellanox Technologies LTD, + Technion - EE Department
Eitan Zahavi*+
Isaac Keslassy+
Avinoam Kolodny+
ANCS 2012

## Slide 2: Big Data – Larger Flows
Data-set sizes keep rising
  Web2 and Cloud Big-Data applications
Data Center Traffic changes to:
  Longer, Higher BW and Fewer Flows
Google

## Slide 3: Static Routing of Big-Data = Low BW
Static Routing cannot balance a small number of flows
Congestion: when BW of link flows > link capacity
When longer and higher-BW flows contend:
  On lossy network: packet drop → BW drop
  On lossless network: congestion spreading → BW drop
Data flow
SR

## Slide 4: Traffic Aware Load Balancing Systems
Centralized
  Flows are routed according to a “global” knowledge
Distributed
  Each flow is routed by its input switch with “local” knowledge
Central Routing Control
SR
SR
SR
Adaptive Routing adjusts routing to network load
Self Routing
Unit

## Slide 5: Central vs. Distributed Adaptive Routing
Distributed Adaptive Routing is either scalable or have global knowledge
It is Reactive
Property | Central Adaptive Routing | Distributed Adaptive Routing
Scalability | Low | High
Knowledge | Global | Local (to keep scalability)
Non-Blocking | Yes | Unknown

## Slide 6: Research Question
Can a Scalable Distributed Adaptive Routing System perform like centralized system and produce non-blocking routing assignments in reasonable time?

## Slide 7: Trial and Error Is Fundamental to Distributed AR
Randomize output port – Trial 1
Send the traffic
Contention 1
Un-route contending flow
  Randomize new output port – Trial 2
Send the traffic
Contention 2
Un-route contending flow
  Randomize new output port – Trial 3
Send the traffic
Convergence!
SR
SR
SR

## Slide 8: Routing Trials Cause BW Loss
Packet Simulation:
R1 is delivered followed by G1
R2 is stuck behind G1
Re-route
R3 arrives before R2
Out-of-Order Packets delivery!
Implications are significant drop in flow BW
  TCP* sees out-of-order as packet-drop and throttle the senders
  See “Incast” papers…
  * Or any other reliable transport
R1
R1
G1
R2
SR
SR
SR
R3

## Slide 9: Research Plan
Given
Analyze Distributed Adaptive Routing systems
Find how many routing trials are required to converge
Find conditions that make the system reach a non-blocking assignment in a reasonable time
t
events
New Traffic
Trial 1
Trial 2
Trial N
No Contention

## Slide 10: A Simple Policy for Selecting a Flow to Re-Route
At each time step
  Each output switch
    Request re-route of a single worst contending flow
At t=0 New traffic pattern is applied
Randomize output-ports and Send flows
At t=0.5 Request Re-Routes
Repeat for t=t+1 until no contention
1
m
1
r
SR
SR
SR
1
n
1
n
input
switch
output
switch

## Slide 11: Evaluation
Measure average number of iterations I to convergence
I is exponential with system size !

## Slide 12: A Balls and Bins Representation
Each output switch is a “balls and bins” system
Bins are the switch input links, balls are the link flows
Assume 1 ball (=flow) is allowed on each bin (=link)
  A “good” bin has ≤ 1 ball
  Bins are either “empty”, “good” or “bad”
SR
SR
SR
1
m
empty
bad
good
Middle Switch

## Slide 13: System Dynamics
Two reasons of ball moves
  Improvement or Induced-move
Balls are numbered by their input switch number
1
2
3
Middle Switch: 1 2 3 4
Output switch 1
3
Induced
2
1
3
Middle Switch: 1 2 3 4
Output switch 2
Improve
2
1
3
4
2
1
3
SW2
SW1
SW3
3

## Slide 14: The “Last” Step Governs Convergence
Estimated Markov chain models
  What is the probability of the required last Improvement to not cause a bad Induced move?
  Each one of the r output-switches must do that step
  Therefore convergence time is exponential with r
1
0
A
B
C
D
Good
Bad
1
0
A
B
C
D
Good
Bad
Output switch 1
Output switch 2
1
0
A
B
C
D
Good
Bad
Output switch r
Absorbing – 1
Absorbing

## Slide 15: Introducing p
Assume a symmetrical system: flows have same BW
What if the Flow_BW < Link_BW?
The network load is Flow_BW/Link_BW
p = how many balls are allowed in one bin
SR
p=1
p=1
p=2
p=2
SR
SR

## Slide 16: p has Great Impact on Convergence
Measure average number of iterations I to convergence
I shows very strong dependency on p

## Slide 17: Implementable Distributed System
Replace congestion detection by flow-count with QCN
  Detected on middle switch output – not output switch input
Replace “worst flow selection” by congested flow sampling
Implement as extension to detailed InfiniBand flit level model

## Slide 18: 52% Load on 1152 nodes Fat-Tree
No change in number of adaptations over time !
No convergence

## Slide 19: 48% Load on 1152 nodes Fat-Tree
t [sec]
Switch Routing Adaptations/ 10usec

## Slide 20: Conclusions
Study: Distributed Adaptive Routing of Big-Data flows
Focus on: Time to convergence to non-blocking routing
Learning: The cause for the slow convergence
Corollary: Half link BW flows converge in few iterations
Evaluation: 1152 nodes fat-tree simulation reproduce these results
  Distributed Adaptive Routing of Half Link_BW Flows is both Non-Blocking and Scalable