## Slide 1: CNSM 2014 SAL: Scaling Data Centers Using Smart Address Learning
Alex Shpiner (Technion / Mellanox) Isaac Keslassy (Technion) Carmi Arad (Marvell) Tal Mizrachi (Marvell) Yoram Revah (Marvell)

## Slide 2: SAL: Scaling Data Centers Using Smart Address Learning
The Problem: VM Address Resolution
in Multi-Tenant Data Centers

## Slide 3: Data Center Network
Address Resolution
Where is VM X???
(Address Resolution)
Location | VM
… | …
… | …
… | X
… | …
… | …
… | …
VM X

## Slide 4: Scalability Problem
Goal: Address resolution that supports VM migrations.
Two scalability bottlenecks:
Table size of resolution entries.
Network load (bandwidth and processing) of resolution packets.
Tradeoff between bottlenecks:
  Smaller tables lower hit-rate more resolution request packets

## Slide 5: Address Resolution Methods
Conventional network implementation alternatives:
  Layer 2 Ethernet: single LAN.
    ARP broadcast flooding
    Large switching tables
    Spanning tree
  Layer 3 IP: subnet for each rack.
    No transparent VM migration between subnets (requires IP address change).
      Interrupts active connections.
      Affects user transparency/isolation/virtualization.
  Overlay Network (next slide)

## Slide 6: Overlay Network
Assign for each VM:
  Application Address (AA)
    VM identity in the virtual tenant space
    Usually combined from tenant ID and VM ID
  Location Address (LA)
    VM identity in the physical network infrastructure
  Both can be MAC or IP addresses.
[VXLAN, NVGRE, VL2, Portland, SEATTLE, SecondNet, etc.]

## Slide 7: Overlay Network
Encapsulation point:
  Encapsulate the packet with additional header or Rewrite existing header fields.
  ToR switch or hypervisor (server).
  We denote it as Edge Bridge (EB).
[VXLAN, NVGRE, VL2, Portland, SEATTLE, SecondNet, etc.]

## Slide 8: Overlay Network
[VXLAN, NVGRE, VL2, Portland, SEATTLE, SecondNet, etc.]

## Slide 9: Address Resolution Methods (Related Work)
How to build the AA-LA resolution table?
Central DB (VL2 [Greenberg et al., 2009], Portland [Niranjan Mysore et al., 2009], SEATTLE (DHT-based) [Kim et al., 2008])
Pull (EtherProxy [Elmeleegy et al., 2009], Diverter [Edwards et al., 2009], SARP [Nachum et al., 2012])
Push (Netlord [Mudigonda et al., 2011])

## Slide 10: Central DB
Drawbacks:
  Computation and communication hot-spot
  Data base consistency maintainence (fast updates, back-up)
  Additional latency to resolve the first packet
?
!
Learn LA(VM 2)
VM 1
VM 2
e.g.: VL2 [Greenberg et al., 2009], Portland [Niranjan Mysore et al., 2009], SEATTLE (DHT-based) [Kim et al., 2008]

## Slide 11: Pull (On-Demand Update)
Drawbacks:
  Broadcasts / flooding
  Additional latency to resolve the first packet
?
?
?
!
Learn LA(VM 1) ?
Learn LA(VM 1) ?
Learn LA(VM 1) ?
VM 1
Learn LA(VM 2)
e.g.: EtherProxy [Elmeleegy et al., 2009], Diverter [Edwards et al., 2009], SARP [Nachum et al., 2012]
VM 2

## Slide 12: Push (On-Change Update)
Drawbacks:
  Unnecessary update messages.
  Large resolution tables in EBs.
    Combining with Pull is possible (but then adds drawbacks from Pull).
!
!
Learn LA(VM 2)
Learn LA(VM 2)
Learn LA(VM 2)
Learn LA(VM 2)
e.g.: Netlord [Mudigonda et al., 2011]

## Slide 13: Scalability Problem
Existing algorithms do not solve the two scalability bottlenecks:
Table size of resolution entries.
Network load of resolution broadcasts.

## Slide 14: Our suggestion for Multi-Tenant DC: Smart Address Learning (SAL)
  Main observation: VMs of different tenants do not communicate between each other.
In resolution table of EB, learn only the VMs of the tenants that run over the EB.
Pull and Push variants.
Benefits:
  Smaller resolution tables (or better hit rate)
  Less request/update broadcasts
  No hot-spots
Selectively learn and update
based on the VM tenancy

## Slide 15: SAL - Pull
?
?
?
!
VM 1
VM 2
VM 3
Learn LA(VM 1)
Learn LA(VM 1)
Do NOT Learn LA(VM 1)
Three VMs of the tenant:
EBs do not learn unneeded addresses.
Improves table hit rate.

## Slide 16: SAL - Push
Update broadcast replaced by unicasts.
Reduces network load.
!
No update message to here
Forget LA(VM 1)
Learn LA(VM 1)
Update LA(VM 2)
Two VMs of the tenant:

## Slide 17: Simulation Settings: Typical Values
Sources: Amazon AWS, CloudNaas [T. Benson et al., 2011], SecondNet [C. Guo et al., 2010], [N. Ilyadis, 2012], [R. Katz, 2009], [J. & A. Meitzler, 2010/12], MS Azure, PAST [B. Stephens et al., 2012], Portland [R. Niranjan Mysore et al., 2009], Seawall [A. Shieh et al., 2010], VL2 [A. Greenberg et al., 2009], [Q. Zhang et al., 2010]

## Slide 18: Simulation Results: Network Load vs. Table Capacity
Rate of address resolution packets in the DCN core.
Broadcast packet to k EBs is counted as k packets.
For small tables, the Central DB is the best option, since the EBs do not have enough memory for any other option.
For large tables, the Push approaches are better.
The addition of SAL to Push decreases the network load by order of magnitude.
Based on typical values.
Network load is in [pkts/sec]
EB Table Capacity
The addition of SAL to Pull and to Push decreases the network load by order of magnitude.

## Slide 19: Simulation Results: Hit Rate vs. Table Capacity
SAL improves the hit rate of the resolution tables.
Percentage of hits in the EB resolution tables.
Based on typical values.
EB Table Capacity

## Slide 20: Analytical Model: Network Load
Rate of address resolution packets in the core.
Broadcast packet to k EBs is counted as k packets.

## Slide 21: Analytical Model: Network Load vs. Number EBs
Number of tenants and VMs scales with number of EBs
Round-robin placement
Push with SAL is scalable, if keeping the fixed.
Based on typical values.
Network load is in [pkts/sec]

## Slide 22: Summary of Contributions
Smart Address Learning (SAL).
  Expands the scalability of address resolution mechanisms, for both the network load and the resolution table sizes.
  The key property: selectively learn the addresses in the resolution tables, based on the fact that the VMs of different tenants do not communicate.
Analytical model of the network load and resolution table sizes for the presented resolution methods.
  Evaluation of the network load and the resolution table size tradeoff using the model and simulations.
Both the network load and the resolution table sizes can be reduced by orders of magnitude.

## Slide 23: Thank you.