## Slide 1: Memento: Making Sliding Windows Efficient for Heavy Hitters
Ran Ben Basat (Harvard University),
Gil Einziger (Ben Gurion University), Isaac Keslassy (VMWare and Technion), Ariel Orda and Shay Vargaftik (Technion), and Erez Waisbard (Nokia Bell Labs)

## Slide 2: Distributed Denial of Service

## Slide 3: Heavy Hitters
How many packets has sent?
Which flows are larger than ?
Traditionally – must fit in the SRAM
0
1
5
3
7
8
8
7
0
1
4
3
7
8
2
7
0
1
5
3
7
8
8
7
0
1
4
3
7
8
2
7
0
1
4
3
7
0
1
5
3
7
8
8
7
0
1
4
3
7
8
2
7
0
1
4
3
7
8
2
7
0
1
4
3
7
0
1
5
3
7
8
8
7
0
1
4
3
7
8
2
7
Can’t allocate a counter for each flow!
Year | 2012 | 2014 | 2016
SRAM (MB) | 10-20 | 30-60 | 50-100
(SilkRoad, SIGCOMM 2017)

## Slide 4: Hierarchical Heavy Hitters (HHH)
LADS: Large-scale Automated DDoS Detection System.
USENIX ATC 2006
DREAM: dynamic resource allocation for software-defined Counting.
ACM SIGCOMM 2014
Automatically Inferring Patterns of Resource Consumption in Network Traffic.
ACM SIGCOMM 2003
Hierarchical Heavy Hitters
identify traffic clusters.
DDoS attack (Aug. 2014)
If we find the attacking networks we can stop the attack!

## Slide 5: DDoS Mitigation
Can we block only the attacking devices?

## Slide 6: Deterministic HHH
Compute all prefixes
Level0 Counting
Level1 Counting
Level2 Counting
Level3 Counting
Level4 Counting
181.7.20.6
181.7.20.6
181.7.20.*
181.7.*.*
181.*.*.*
*.*.*.*
Level1 Counting
Level0 Counting
Level2 Counting
Level3 Counting
Level4 Counting
“Count each prefix independently.”
Mitzenmacher et al., Hierarchical Heavy Hitters with the Space Saving Algorithm, ALENEX 2012

## Slide 7: Randomized HHH
Compute a random prefix
Level0 Counting
Level1 Counting
Level2 Counting
Level3 Counting
Level4 Counting
181.7.20.*
Level1 Counting
“Select a prefix at random and count it”
Ben Basat et al., Constant Time Updates in Hierarchical Heavy Hitters, ACM SIGCOMM 2017
181.7.20.6

## Slide 8: From Streams to Sliding Windows – the heavy hitters case
0
1
5
3
7
8
8
7
0
1
4
3
7
8
2
7
0
1
5
3
7
8
8
7
0
1
4
3
7
8
2
7
0
1
4
3
7
0
1
5
3
7
8
8
7
0
1
4
3
7
8
2
7
0
1
4
3
7
8
2
7
0
1
4
3
7
0
1
5
3
7
8
8
7
0
1
4
3
7
8
2
7
0
0
1
4
3
7
8
2
7
0
1
4
3
7
0
1
5
3
7
8
8
7
0
1
4
3
7
8
2
7
A stream of elements
How many times have 7 appeared within the last W items?
elements

## Slide 9: Why Sliding Windows?
Often, we only care about the recent data.
  Sliding windows detect new heavy hitters quicker.
They were considered in the past
  “it may be desirable to compute HHHs over only a sliding window of the last n items” (Mitzenmacher et al., 2012)
And were dismissed as
  “markedly slower and less space-efficient in practice”

## Slide 10: Sliding Windows Algorithms have Improved – the WCSS algorithm
Ben Basat et al., Heavy Hitters in Streams and Sliding Windows, IEEE INFOCOM 2016

## Slide 11: Markedly slower and less space-efficient in practice?
Compute all prefixes
WCSS
WCSS
WCSS
WCSS
WCSS
181.7.20.6
181.7.20.6
181.7.20.*
181.7.*.*
181.*.*.*
*.*.*.*
“Count each prefix independently.”
Mitzenmacher et al., Hierarchical Heavy Hitters with the Space Saving Algorithm, ALENEX 2012
Almost as fast as the (non-window) MST algorithm.
But far slower than RHHH.

## Slide 12: Strawman #1
Compute a random prefix
WCSS (W/5)
WCSS (W/5)
WCSS (W/5)
WCSS (W/5)
WCSS (W/5)
181.7.20.6
181.7.20.*
“Select a prefix at random and count it”
Problem:
The WCSS instances go out of sync

## Slide 13: Strawman #2
181.7.20.6
“Flip a coin to choose if to update”
Add with probability
Otherwise
discard
Problem:
Instead of looking at W packets this reflects

## Slide 14: Challenges
How to apply sampling for accelerating sliding window algorithms?
How to keep synchronization and reflect exactly packets?
In addition, we want extend the single-switch solution to network-wide monitoring.

## Slide 15: Memento – Efficient HH on Sliding Windows
Key idea: decouple the (lightweight) sliding operation from the (computationally expensive) counting step.

## Slide 16: Performance Evaluation on Internet Traces
Ben Basat et al., Heavy Hitters in Streams and Sliding Windows, IEEE INFOCOM 2016

## Slide 17: En route to HHH - Strawman #3
Compute all prefixes
Memento
Memento
Memento
Memento
Memento
181.7.20.6
181.7.20.6
181.7.20.*
181.7.*.*
181.*.*.*
*.*.*.*
“Count each prefix efficiently .”
Still requires update time
(but independently)

## Slide 18: H-Memento – HHH on Sliding Windows
Memento
181.7.20.13
Random prefix
H-Memento
181.7.20.*
“One prefix, one data structure.”
Same space as previous works, different structure
¥
¥

## Slide 19: H-Memento – HHH on Sliding Windows

## Slide 20: H-Memento – HHH on Sliding Windows (CoNEXT 2018)

## Slide 21: D-Memento – From single node to network wide
“Distributed Sliding Window”: reflect the last W packets that were measured anywhere in the network
No (direct) communication between measurement nodes
Minimal control bandwidth (configurable)
Operators care about the entire network and require network-wide view.
  port scans and superspreaders are not identifiable from a single node.
Different nodes may have different traffic rates

## Slide 22: D-Memento – From single switch to network wide

## Slide 23: D-Memento – From single switch to network wide
Aggregation: run a local algorithm at each point and sync with the controller as frequently as possible.
Sample: each measurement point samples each packet with probability and sends samples to the controller that runs H-Memento.
Batch: collect samples before sending the report.
  Increases the effective sampling rate.
  Introduces reporting delay.

## Slide 24: Evaluation: Distributed HTTP Flood attack using limited resources
How can we simulate O(10K) stateful connections from “distinct” IP addresses using a single attacking device?

## Slide 25: Evaluation: Distributed HTTP Flood attack using limited resources
How can we simulate O(10K) stateful connections from “distinct” IP addresses using a single attacking device?
Attacker side:
Server side:
Create a mapping between port numbers and source IPs
In egress, translate from port number to determine “source” IP
  Make sure to compute checksum, etc.
At ingress, translate from destination IP to port number
Change IP tables to redirect all packets back to the attacker’s interface.

## Slide 26: Evaluation: Distributed HTTP Flood attack using limited resources
We use legitimate data and inject malicious traffic from 50 random 16-bit subnets which make up for 70% of the traffic.
We deployed 10 HAProxy load balancer instances that report to a centralized controller using 1 byte/request control bandwidth.
The attackers perform a TCP handshake and send an HTTP POST request.

## Slide 27: Evaluation: Distributed HTTP Flood attack using limited resources

## Slide 28: Conclusions
Sliding window solutions can be (nearly) as efficient as interval ones.
We extended HAProxy to network rate-limiting.
  Open source: https://github.com/DHMementoz/Memento
Memento provides a measurement infrastructure for DDoS identification, mitigation, and evaluation.

## Slide 29: Any Questions

## Slide 30: Any Questions

## Slide 31: Any Questions

## Slide 32: Any Questions

## Slide 33: Any Questions

## Slide 34: Any Questions

## Slide 35: Any Questions