## Slide 1: How I Learned to Stop Worrying About the Core and Love the Edge
Aditi Ghag2
Naga Katta1,2, Mukesh Hira2, Changhoon Kim3, Isaac Keslassy2,4, Jennifer Rexford1
1Princeton University, 2VMware, 3Barefoot Networks, 4Technion
CLOVE

## Slide 2: Data center load balancing today
Equal-Cost Multi-Path (ECMP) routing:
Path(packet) = hash(5-tuple{src,dst IP + src,dst port + protocol number})
Hash collisions
Coarse-grained
Congestion-oblivious
. . . . . .
…
…
…
Servers
Leaf
Switches
Spine
Switches

## Slide 3: Proposed load balancing schemes
Hypervisors
Centralized load balancing
Hedera, MicroTE, SWAN, Fastpass
Slow reaction time
Routes computation overhead
vSwitch
vSwitch
Central Controller

## Slide 4: Proposed load balancing schemes
Hypervisors
CONGA, HULA
Needs custom ASIC data center fabric
High capital cost
vSwitch
vSwitch
In-network load balancing

## Slide 5: Proposed load balancing schemes
Hypervisors
vSwitch
vSwitch
PRESTO
Non-standard shadow mac labels based forwarding
Controller intervention in case of asymmetry
MPTCP
Incast collapse
Guest VM network stack changes
End-host load balancing

## Slide 6: vSwitch as the sweet spot
vSwitch
vSwitch
Payload
IP
Eth
Eth
IP
TCP
Overlay
Network switches with ECMP using 5-tuple
Outer transport source ports are used for ECMP traffic distribution
Spine
switches
Leaf
switches

## Slide 7: CLOVE design
Path discovery
Load-balancing flowlets
vSwitch load-balancing

## Slide 8
Path Discovery
Standard ECMP in the physical network
vSwitch
vSwitch
Hypervisor H1
Hypervisor H2
Hypervisor learns source port to path mapping
Dst | SPort
H2 | 5001
H2 | 5002
H2 | 5003
H2 | 5004
H1 to H2
DPort: Fixed
SPort: P1
Overlay
Data
H1 to H2
DPort: Fixed
SPort: P2
Overlay
Data
H1 to H2
DPort: Fixed
SPort: P3
Overlay
Data
H1 to H2
DPort: Fixed
SPort: P4
Overlay
Data
H1
H2
Load balancing flowlets
vSwitch Load balancing
Outer transport source port maps to network path

## Slide 9
Load balancing flowlets
vSwitch
vSwitch
Eth
IP
TCP src 5001
Overlay
Data
Eth
IP
TCP src 5002
Overlay
Data
Dst | SPort
H2 | 5001
H2 | 5002
H2 | 5003
H2 | 5004
H2
H1
Flowlet gap
Eth
IP
TCP src 5003
Overlay
Data
Eth
IP
TCP src 5004
Overlay
Data
Path Discovery
vSwitch Load balancing

## Slide 10: Edge-Flowlet
Flowlet splitting in vSwitch
Select learnt source port for flowlets at random
Physical switches forward flowlets using ECMP

## Slide 11
Dst | SPort | Wt
H2 | 5001 | 0.25
H2 | 5002 | 0.25
H2 | 5003 | 0.25
H2 | 5004 | 0.25
Path weight table
Data
Dst | SPort | Wt
H2 | 5001 | 0.1
H2 | 5002 | 0.3
H2 | 5003 | 0.3
H2 | 5004 | 0.3
2. Switches mark ECN on data packets
vSwitch
vSwitch
Hypervisor H1
Hypervisor H2
1. Src vSwitch detects and forwards flowlets
3. Dst vSwitch relays ECN and src port to src vSwitch
5. Src vSwitch adjusts path weights for the src port
4. Return packet carries ECN and src port for forward path
vSwitch Load balancing
CLOVE-ECN
Path Discovery
Load balancing flowlets
Congestion-aware balancing based on ECN feedback

## Slide 12
vSwitch Load balancing
CLOVE-INT
Load balancing flowlets
Path Discovery
Data
Dst | SPort | Util
H2 | 5001 | 40
H2 | 5002 | 30
H2 | 5003 | 50
H2 | 5004 | 10
2. Switches add requested link utilization
vSwitch
vSwitch
Hypervisor H1
Hypervisor H2
1. Src vSwitch adds INT instructions to flowlets
3. Dst vSwitch relays link utilization and src port to src vSwitch
5. Src vSwitch updates link utilizations
4. Return packet carries link utilization for forward path
6. Src vSwitch forwards flowlets on least utilized paths
Utilization-aware balancing based on INT feedback

## Slide 13: Performance evaluation setup
Implementation in ns-2 simulator
Realistic Web Search Workload
Client on Leaf1 <-> server on Leaf2
…
…
16 Clients
Spine1
Spine2
Leaf1
4 x 4 Gbps
16 x 1 Gbps
16 Servers
Leaf2

## Slide 14: Symmetric topology
CLOVE-ECN captures 82% of the performance gain between ECMP and CONGA
1.1x higher FCT than CONGA
1.4x lower FCT than ECMP

## Slide 15: Asymmetric topology
1.2x higher FCT than CONGA
CLOVE-ECN captures 80% of the performance gain between ECMP and CONGA
3x lower FCT than ECMP

## Slide 16: CLOVE highlights
Captures 80% of the performance gain of CONGA
No changes to data center infrastructure or guest VM
Adapts to asymmetry without any controller input
Scalable due to distributed state
Modular implementation

## Slide 17: Future work
Use packet latency to infer congestion
Adapt flowlet-gap to network conditions
Fine-tune congestion-management algorithm
Stability
Analyze processing overhead

## Slide 18
THANK YOU
Questions?