## Slide 1: Providing Performance Guarantees in Multipass Network Processors
Isaac Keslassy | Kirill Kogan | Gabriel Scalosub | Michael Segal
Technion | Cisco & BGU (Ben-Gurion University) | BGU | BGU

## Slide 2: Network Processors (NPs)
NPs used in routers for almost everything
  Forwarding
  Classification
  DPI
  Firewalling
  Traffic engineering
Classical NP architectures
  Homogeneous tasks
   Increasingly heterogeneous demands
    Examples: VPN encryption, LZS decompression, advanced QoS, …
What are “classical NP architectures”?

## Slide 3: Pipelined NP Architecture
Each packet gets processed by a pipeline of PPEs (packet processing engines)
  each PPE in charge of a different task
 main issues: hard to scale, synchronous, packet header copy
PPE
PPE
PPE
PPE
PPE
PPE
Packet Header Buffer
E.g., Xelerated X11 NP

## Slide 4: Parallel/Multi-Core NP Architecture
Each packet is assigned to a single PPE
  single PPE performs all processing, in “run-to-completion”
 main issue: run-to-completion  heavy packets can starve light ones
PPE
PPE
PPE
Hybrid Architecture:
Pipeline + Multi-core
E.g., Cavium CN68XX NP
E.g., EZChip NP-4 NP

## Slide 5: Multipass NP Architecture
Packet processing divided into processing cycles
Packet headers recycled into the queue after each processing cycle
 Main benefits:
  More scalable
  Asynchronous
  No run-to-completion (heavy packets do not necessarily starve light ones)
 Main issue : many degrees of freedom (more complex scheduling)
E.g., Cisco QuantumFlow NP
PPE
PPE
PPE
Packet Header Buffer

## Slide 6: Scheduling in Multipass NP
Packets have heterogeneous demands
  Each packet might require a different number of cycles
Designer objective: guarantee minimum throughput
  Minimum number of processed packets per second
Problem: many degrees of freedom
  Buffer management: FIFO, priority queueing, …? Preemption upon full buffer?
  For each packet: what PPEs? In what order?
  Fairness?
  No reordering?
  Heterogeneous PPEs?
PPE
PPE
PPE
Packet Header Buffer

## Slide 7: Assumptions
  Focusing on buffer management policy
  Efficiently use the full buffer size (unit-size packets with slotted time)
Only 1 PPE
  Complex enough!
Each packet needs up to k passes
  Number of passes known for each packet
  k used in analysis, not in algorithm
Our goal: competitive worst-case throughput guarantee
  For any input sequence σ, show that Throughput(σ) ≥ OPT(σ) / c
  Arbitrary arrival sequences (adversarial…)

## Slide 8: Buffer Management Policies
PPE
2
2
4
5
5
5
1
1
PPE
2
2
4
5
5
5
1
1
1
PQ (Priority queueing)
less work = higher priority
FIFO
1

## Slide 9: A Case for Preemption
Assume non-preemption
  when a packet arrives to a full buffer, it is dropped
FIFO lower bound
  simple traffic pattern: competitive ratio is (k)
PQ lower bound
  (much) more involved
  also (k)
(OR, how bad can non-preemption be when buffer overflows?)
Matching O(k) upper bounds for both

## Slide 10: What If We Preempt?
PPE
2
2
4
5
5
5
3
Example:

## Slide 11: What If We Preempt?
Preemption + PQ = Optimal
  PQ can serve as a benchmark for optimality
Preemption + FIFO?
  not optimal: (log k) lower bound
  sublinear(k) upper bound: still open

## Slide 12: Are Preemptions Free?
New packets “cost” more than recycled packets
  Example: costly memory access and system updates (pointers, data-structures)
Copying cost 
  each new packet admitted incurs a cost of [0,1)
Objective:
  maximize ( Throughput – Cost )

## Slide 13: Algorithm PQ
PPE
2
2
4
5
10
30
29
When buffer full, accept new packet if it needs less cycles than (worst packet / β)
13
Example: β =2

## Slide 14: Algorithm PQ
Competitive ratio: f(k,,)
Gives some best  for each value of k and 
(1- ) (1 + log/(-1)(k/2) + log(k))
1-  log(k)

## Slide 15: Simulation Results
Single PPE (C=1), copying cost =0.4
  ON-OFF bursty traffic
PQ is NOT optimal anymore!
k

## Slide 16: Conclusion
Multipass NP architecture model
Preemptions help significantly
If preemptions are not free, schedule optimality gets complicated

## Slide 17: Thank you.