## Slide 1: Dragonfly: In-Flight Congestion Control Identification
Dean Carmel, Isaac Keslassy
Department of Electrical & Computer Engineering Technion

## Slide 2: Motivation: TCP Congestion
Egress
Ingress
CUBIC
RENO
Identify congestion control variant
BBR

## Slide 3: Motivation: TCP Congestion
We need to classify. Why?
Flow classification is essential for identifying the causes of congestion that would otherwise remain unknown.
Through classification, we can select optimal congestion management techniques by considering the unique congestion control algorithms utilized by each flow.

## Slide 4: Motivation: TCP Congestion
BBR
CUBIC
RENO
BBR
CUBIC
RENO
Flow classification is essential for identifying the causes of congestion that would otherwise remain unknown.
Through classification, we can select optimal congestion management techniques by considering the unique congestion control algorithms utilized by each flow.

## Slide 5: Wishlist
1. We are allowed to inspect the ingress and egress of the buffer only.
2. Online: on-the-fly, starting from any point in time.
3. Scalable traffic collection: input computation complexity should be in 𝑂(1) for each slot.
4. Scalable classification: simple neural-network architecture.
5. Reliable classification: resilient to different settings.

## Slide 6: Related Work
  Programable dataplanes for fast classification.
  Congestion control identification variants using packet arrival time information.

## Slide 7: Dragonfly Algorithm
Inputs Per Packet
Aggregated inputs per (1ms) slot
Classification (CNN)
Output: classified CCA

## Slide 8: Dragonfly Algorithm
Classification
Per Packet
Per Slot
Dataframe
CBIQ=
congestion bytes in queue

## Slide 9: Dragonfly Algorithm
CBIQ = 1
Capture Time Gap
Egress
Ingress
Out Throughput
In Throughput
CBIQ = 3
CBIQ=
congestion bytes in queue

## Slide 10: Dragonfly Algorithm
Need for Built-in Memory: CBIQ “remembers" the past by measuring the queue size devoted to the analyzed flow, thus implicitly relying on an integral of the past throughput.
In addition, the built-in memory in CBIQ helps us because it can reduce the volatility of the input.
100ms
60s

## Slide 11: Dragonfly Algorithm
BBR
CUBIC
RENO

## Slide 12: Dragonfly Algorithm
A single TCP flow
CBIQ
Throughput

## Slide 13: Dragonfly Algorithm
b. BBR
c. CUBIC
a. RENO

## Slide 14: Classification
60 seconds session, 15 background flows

## Slide 15: Classification
60 seconds session, random sub-interval of 100ms, 15 background flows

## Slide 16: CNN
X5
conv2D
BN
RelU
MaxPool
init weights
Dataframe
Classification
Input Size:
Interval Length X 2
Output Size: 3
{CBIQ, Throughput}
Inputs
{BBR, Cubic, Reno}
Outputs

## Slide 17: Dragonfly Algorithm
eBPF
1. Fast header extraction
2. Dynamic filtering decision

## Slide 18: Dragonfly Algorithm

## Slide 19: Sampling
First-packet sampling
For each flow, eBPF keeps the first packet of each time slot and drops the other packets.
Reducing both the raw- input dictionary size and the computation complexity.
5 MB table size

## Slide 20: Simulations & Experiments
Linux- based router.
Buffer size of 2000- 16000 packets.
Queueing delay of 25- 200 ms.
server
rtr
Router
{0, 15, 30, 60, 75}
Background flows

## Slide 21: Impact of sub-interval duration
60 seconds session, 15 background flows

## Slide 22: Impact of background traffic
60 seconds session

## Slide 23: Running in the cloud
We first install 3 AWS servers in Tokyo, N. California and Frankfurt.
We use three clients as three flow sources:
  Each client uses a distinct 10- Gbps line to connect to a shared router, which uses a 1- Gbps line to get to the Internet.
rtr
source
destination

## Slide 24: Impact of sub-interval duration in the cloud
60 seconds session, 15 background flows

## Slide 25: Conclusion
We introduced CBIQ which contains a built- in intrinsic memory.
We further designed an eBPF- based scalable traffic collection.
We evaluated Dragonfly using a variety of platforms which has outperformed exiting works, including Deepcci.