## Slide 1: Simulate Before Sending: Rethinking Transport in Datacenter Networks
Dan Straussman
Isaac Keslassy
Alexander Shpiner
Liran Liss

## Slide 2: Motivation
Challenge: datacenters designed for AI training
AI training applications are very bursty
Mixture-of-experts (MoE) models exhibit unpredictable patterns
Worsen packets drops
Increase CCTs
Increase tail latency of RDMA
Motivation
DCSIM
Evaluation
Conclusion

## Slide 3: Current Solutions
Per-packet load balancing
Random packet spraying (Alibaba Stellar), Adaptive packet spraying (STrack, REPS, Ultra Ethernet Consortium), Adaptive routing (NVIDIA’s Spectrum-X)
  Relies on commodity switches
  Vulnerable to losses
Credits
Receiver-driven credit-based scheme that attempts to avoid losses (ExpressPass, Homa, Aeolus, FlexPass)
  Handles incast
  No visibility into network
Motivation
DCSIM
Evaluation
Conclusion

## Slide 4: Current Solutions
Scheduling-based approach
Shifts scheduling decisions to end hosts using matching (dcPIM, pHost)
  High utilization and scalability
  No visibility into network
Reservation
Per-flow fixed-bandwidth reservations (Harmony)
  Eliminates congestion-related drops
  Needs specialized switches
Motivation
DCSIM
Evaluation
Conclusion

## Slide 5: Our Goal
To design transports that lower CCTs by making commodity lossy networks practically lossless.
Per-Packet Reservations
Commodity Switches
Motivation
DCSIM
Evaluation
Conclusion

## Slide 6: DCSIM Idea
Shadow simulation network:
1/100th the rate of our real network
SIM packets 100 times smaller than real-network DATA packets
Same propagation, transmission and queuing delays
 Not practical
Motivation
DCSIM
Evaluation
Conclusion
Shadow network
Real network

## Slide 7: DCSIM Idea
Approximate shadow simulation network using dedicated buffers:
DATAs and SIMs (SIM-ACKs) coexist in the same network
Each SIM effectively implements reservation on a given path for a place in the DATA buffers that will be used when sending a DATA some fixed time later - RTTmax
Motivation
DCSIM
Evaluation
Conclusion
RTTmax

## Slide 8: DCSIM Idea
 2 ready DATA pkts  send SIM1 (red path) and SIM2 (green path)
 Queue full  SIM1 dropped
 SIM2 received  send SIM-ACK2 (arbitrary path)
 SIM-ACK2 received  Send 1st DATA pkt on green path
S
D
Motivation
DCSIM
Evaluation
Conclusion
➄ Sending DATA-ACK packets

## Slide 9: DCSIM Commodity Switches
Any SIM that arrives at the SIM buffer enters the queue if there is space, and is
dropped otherwise.
Once a SIM reaches D, D sends back a SIM-ACK to S.
SIMs (serviced at the highest priority) are rate-limited using a token bucket.
Motivation
DCSIM
Evaluation
Conclusion

## Slide 10: DCSIM Challenge
DATAs may be dropped in multi-stage networks
A
B
C
A
B
C
SIM phase
Motivation
DCSIM
Evaluation
Conclusion

## Slide 11: DCSIM Challenge
DATAs may be dropped in multi-stage networks
A
B
C
A
B
C
drop
SIM phase
Motivation
DCSIM
Evaluation
Conclusion

## Slide 12: DCSIM Challenge
DATAs may be dropped in multi-stage networks
A
B
C
A
C
SIM phase
Motivation
DCSIM
Evaluation
Conclusion

## Slide 13: DCSIM Challenge
DATAs may be dropped in multi-stage networks
A
B
C
A
C
DATA phase
Motivation
DCSIM
Evaluation
Conclusion

## Slide 14: DCSIM Challenge
DATAs may be dropped in multi-stage networks
In evaluations, we found that if the DATA buffer can hold about 2× as many packets as the SIM buffer, then we could not see a single DATA loss
A
B
C
A
C
drop
DATA phase
Motivation
DCSIM
Evaluation
Conclusion

## Slide 15: DCSIM Evaluation
We employ a 3-layer fat-tree topology with
  128 hosts
  800 Gbps links
  9 KB jumbo frames
We compare dcSim against pFabric, pHost and dcPIM.
We focus on collective communication patterns that are representative of AI
  Permutation
  All-to-all
  All-to-all-v
A
B
C
D
E
A
B
C
D
E
Motivation
DCSIM
Evaluation
Conclusion

## Slide 16: DCSIM Evaluation
Rate of DATA packets corresponds indeed to the earlier rate of SIM packets.
Infinite all-to-all traffic pattern.
Motivation
DCSIM
Evaluation
Conclusion

## Slide 17: DCSIM Evaluation
Five all-to-all-v collectives with different average flow sizes.
Motivation
DCSIM
Evaluation
Conclusion
CCT
Loss Rate
Queueing Delay
Reordering

## Slide 18: DCSIM Evaluation
Loss Rate
Queueing Delay
Reordering
Adverse scenario with an oversubscribed network using half the core switches, given
five all-to-all-v collectives.
Motivation
DCSIM
Evaluation
Conclusion
CCT

## Slide 19: DCSIM Evaluation
Sensitivity analysis shows that DCSIM outperforms other algos
Packet size
Buffer size
Number of collectives
Max collective size
Clock drift
Motivation
DCSIM
Evaluation
Conclusion
buffer size

## Slide 20: Conclusion
DCSIM achieves
Low CCTs
Practically lossless
Commodity switches
Shines under adverse conditions
Low queueing
The DCSIM source code is available online
https://github.com/danstr1/dcsim
Motivation
DCSIM
Evaluation
Conclusion